## Slide 1
Uniview NVR Introduction

## Slide 2
01
Product
Overview

## Slide 3
NVR301-08L-P8
02: 2 SATA slots
04: 4 SATA slots
08: 8 SATA slots
16: 16 SATA slots
Series
Network
Video
Recorder
04: 2 Channels
08: 4 Channels
16: 16 Channels
32: 32 Channels
64: 64 Channels
128: 128 Channels
Px: x PoE Ports
NVR Naming Rule
E: Enhanced
L: Plastic
P: PoE

## Slide 4
2 series NVR
NVR Product Line

## Slide 5
NVR201-04/08L(P)
H.264/MJPEG
4/8-ch IP video input
1 SATA up to 6TB
Smart 1U plastic chassis, Fan-less design
4/8 PoE+ ports (-LP)
Model Name | NVR201-04L | NVR201-08L | NVR201-04LP | NVR201-08LP
Incoming Bandwidth | 4-ch / 32Mbps | 8-ch / 64Mbps | 4-ch / 32Mbps | 8-ch / 64Mbps
Decoding Ability | 4 x 1080P 2 x 4MP 1 x 6MP | 8 x 720P 4 x 1080P | 4 x 1080P 2 x 4MP 1 x 6MP | 8 x 720P 6 x 1080P 3 x 4MP 2 x 6MP 1 x 8MP
SATA | 1 | 1 | 1 | 1
PoE | N/A | N/A | 4 | 8
Network Interface | 1 | 1 | 1 | 1

## Slide 6
NVR201-04/08E(P)
H.264/MJPEG
4/8-ch IP video input
1 SATA up to 6TB
Mini 1U metal chassis, Fan-less design
Touch panel
4/8 PoE+ ports (-EP)
Model Name | NVR201-04E | NVR201-08E | NVR201-04EP | NVR201-08EP
Incoming Bandwidth | 4-ch / 32Mbps | 8-ch / 64Mbps | 4-ch / 32Mbps | 8-ch / 64Mbps
Decoding Ability | 4 x 1080P 2 x 4MP 1 x 6MP | 8 x 720P 4 x 1080P 2 x 4MP 1 x 6MP | 4 x 1080P 2 x 4MP 1 x 6MP | 8 x 720P 4 x 1080P 2 x 4MP 1 x 6MP
SATA | 1 | 1 | 1 | 1
PoE | N/A | N/A | 4 | 8
Network Interface | 1 | 1 | 1 | 1

## Slide 7
Model Name | NVR202-08E | NVR202-16E | NVR202-32E | NVR202-08EP | NVR202-16EP
Incoming Bandwidth | 8-ch / 64Mbps | 16-ch / 128Mbps | 32-ch / 200Mbps | 8-ch / 64Mbps | 16-ch / 128Mbps
Decoding Ability | 8 x 720P 4 x 1080P 2 x 4MP 1 x 6MP | 16 x 720P 6 x 1080P 3 x 4MP 2 x 6MP 1 x 8MP | 32 x D1 16 x 720P 6 x 1080P 3 x 4MP 2 x 6MP 1 x 8MP | 8 x 720P 6 x 1080P 3 x 4MP 2 x 6MP 1 x 8MP | 16 x 720P 6 x 1080P 3 x 4MP 2 x 6MP 1 x 8MP
SATA | 2 | 2 | 2 | 2 | 2
PoE | N/A | N/A | N/A | 8 | 8
Network Interface | 1 | 1 | 1 | 1 | 1
NVR202-08/16/32E(P)
H.264/MJPEG
8/16/32-ch IP video input
2 SATA up to 12TB
Mini 1U metal chassis, Fan-less design
Touch panel
8 PoE+ ports (-EP)

## Slide 8
NVR204-16/32E
H.264/MJPEG
16/32-ch IP video input
4 SATA up to 24TB
1U metal chassis
Touch panel
Model Name | NVR204-16E | NVR204-32E
Incoming Bandwidth | 16-ch / 128Mbps | 32-ch / 200Mbps
Decoding Ability | 6 x 1080P | 6 x 1080P
SATA | 4 | 4
Network Interface | 2 | 2

## Slide 9
NVR208-16/32
H.264 / MJPEG
16/32-ch IP video input
8 SATA up to 48TB
2U metal chassis
Touch panel
Dual network interface
Model Name | NVR208-16 | NVR208-32
Incoming Bandwidth | 16-ch / 128Mbps | 32-ch / 200Mbps
Decoding Ability | 6-ch 1080P | 6-ch 1080P
SATA | 8 | 8
Network Interface | 2 | 2
Why we are special?

## Slide 10
3 series NVR
NVR Product Line

## Slide 11
NVR301-04/08/16E
H.265/H.264/MJPEG
4K display output
4/8-ch IP video input
1 SATA up to 6TB
Mini 1U metal chassis, Fan-less design
Model Name | NVR301-04E | NVR301-08E | NVR301-16E
Incoming Bandwidth | 4-ch / 40Mbps | 8-ch / 60Mbps | 4-ch / 80Mbps
Decoding Ability | 4 x 1080P 1 x 4K | 8 x 720P 4 x 1080P 1 x 4K | 16 x D1 8 x 720P 4 x 1080P 1 x 4K
SATA | 1 | 1 | 1
Network interface | 1 | 1 | 1

## Slide 12
NVR304-16/32E
H.265/H.264/MJPEG
4K display output
16/32-ch IP video input
4 SATA up to 24TB
1U metal chassis
Dual network interface
Model Name | NVR304-16E | NVR304-32E
Incoming Bandwidth | 16-ch / 160Mbps | 32-ch / 320Mbps
Decoding Ability | 16 x 1080P 7 x 4MP 4 x 4K | 32 x 720P 16 x 1080P 7 x 4MP 4 x 4K
SATA | 4 | 4
Network Interface | 2 | 2

## Slide 13
NVR304-16/32EP
H.265/H.264/MJPEG
4K display output
16/32-ch IP video input
4 SATA up to 24TB
2U metal chassis
16 PoE+ ports
Model Name | NVR304-16EP | NVR304-32EP
Incoming Bandwidth | 16-ch / 160Mbps | 32-ch / 320Mbps
Decoding Ability | 16 x 1080P 7 x 4MP 4 x 4K | 32 x 720P 16 x 1080P 7 x 4MP 4 x 4K
SATA | 4 | 4
PoE | 16 | 16
Network Interface | 1 | 1
Will be released in 2016.3

## Slide 14
NVR308-32/64E
H.265/H.264/MJPEG
4K display output
32/64-ch IP video input
8 SATA up to 48TB
2U metal chassis
Dual network interface
Model Name | NVR308-32E | NVR308-64E
Incoming Bandwidth | 32-ch / 320Mbps | 64-ch / 320Mbps
Decoding Ability | 32 x 720P 16 x 1080P 7 x 4MP 4 x 4K | 64 x D1 32 x 720P 16 x 1080P 7 x 4MP 4 x 4K
SATA | 8 | 8
Network Interface | 2 | 2

## Slide 15
NVR308-32/64R
H.265/H.264/MJPEG
4K display output
32/64-ch IP video input
8 SATA up to 48TB
RAID1, RAID5, Hot-swappable
2U metal chassis
Dual network interface
Model Name | NVR308-32R | NVR308-64R
Incoming Bandwidth | 32-ch / 320Mbps | 64-ch / 320Mbps
Decoding Ability | 32 x 720P 16 x 1080P 7 x 4MP 4 x 4K | 64 x D1 32 x 720P 16 x 1080P 7 x 4MP 4 x 4K
SATA | 8 | 8
Network Interface | 2 | 2

## Slide 16
5 series NVR
NVR Product Line

## Slide 17
NVR516-64/128
H.265/H.264/MJPEG
4K display output
64/128-ch IP video input
16 SATA up to 96TB
RAID1, RAID5, Hot-swappable
3U metal chassis
4 x Network interface
Powerful decoding ability (Up to 2 decoder card optional)
Model Name | NVR516-64 | NVR516-128
Incoming Bandwidth | 64-ch / 384Mbps | 128-ch / 512Mbps
Decoding Ability (Without decoder card) | 16 x 1080P | 16 x 1080P
Each 4-ch HDMI decoder card | 32 x 1080P | 32 x 1080P
Each 6-ch HDMI decoder card | 48 x 1080P | 48 x 1080P
SATA | 16 | 16
Network Interface | 4 | 4
Will be released in 2016.3

## Slide 18
02
High Light
Features

## Slide 19
High Reliability

## Slide 20
Other Manufacturer
Turn on the NVR
Uniview
51.0℃
After a while
38.9℃
Better Heat Dissipation Effect
Lower temperature inside the case
Lower temperature of the CPU
Lower failure rate
and repair rate

## Slide 21
Fanless Design
Enough of the noise made by your NVR?
UNV NVR201、 NVR202、NVR301
With or without PoE
All with Fanless design
Larger ,ruggedized cooling fin

## Slide 22
Touch Panel
NVR201 series
NVR202 series
NVR204 series
NVR208 series
Dust-proof
Water-proof
Long working life

## Slide 23
Block Storage
Block Storage
No disk fragmentation
No pre-formatting needed
Much higher efficiency
Conventional file system
Storage efficiency limited by
disk fragmentation

## Slide 24
RAID
Disk1
Disk2
Disk3
Disk4
New Disk
Uniview NVR308-32/64R support RAID1, RAID5, even one of the disk get failed, user can replace it by new disk easily, and the video will never lose
NVR308-32/64R Support hot-swap from front panel directly, no need to power off the NVR or open the NVR case, so it is much more convenient and the NVR can keep recording even you are changing the hard disk
Notes: Check code

## Slide 25
Dual Network Interface
2 x Gigabyte Ethernet Interface
NVR
Switch
1.Multi-address mode
Setup two IP addresses for one NVR, connect to two different network (One for local access, another one for remote access)
2.Load Balance mode
Automatically balance the throughout, combine to one 2 Gigabyte Ethernet interface
3.Fault-tolerant mode
Automatically enable the backup port when the main port failed
NVR304 series(Non PoE)
NVR208 series
NVR308 series

## Slide 26
Https
Encrypted network transmission
Http: Easy to be
captured and cracked
Https
UNV NVR all support https, give the data transmission the best protection between NVR and Client

## Slide 27
Easy Installation

## Slide 28
PoE
Traditional camera power up method: By power adapter
Uniview provide PoE NVR(Model name with “P”) which make it much easier and more economic(Don’t need additional power adapter)

## Slide 29
Long Range PoE
100M mode 200m, CAT6
Normally PoE distance is 100m,but with UNV NVR and UNV IP Cameras, it can reach up to 200m (100Mbps) /300m (10Mbps) PoE transmission distance with Cat5E or higher
PoE
IPC Series | Transmit distance |  |  | 
 | 10M mode |  | 100M mode | 
IPC54 series Box Camera | CAT5E 300m | CAT6 300m | CAT5E 150m | CAT6 200m
IPC56 series Box Camera | CAT5E 300m | CAT6 300m | CAT5E 150m | CAT6 200m
IPC24 series Bullet Camera | CAT5E 300m | CAT6 300m | CAT5E 150m | CAT6 200m
IPC34 series Fixed Dome Camera | CAT5E 300m | CAT6 300m | CAT5E 150m | CAT6 200m
IPC21 series Bullet Camera | CAT5E 140m | CAT6 140m | CAT5E 120m | CAT6 120m
IPC22 series Bullet Camera | CAT5E 140m | CAT6 140m | CAT5E 120m | CAT6 120m
IPC23 series Bullet Camera | CAT5E 140m | CAT6 140m | CAT5E 120m | CAT6 120m
IPC32 series Fixed Dome Camera | CAT5E 140m | CAT6 140m | CAT5E 120m | CAT6 120m
IPC36 series Fixed Dome Camera | CAT5E 140m | CAT6 140m | CAT5E 120m | CAT6 120m
10M mode 300m, CAT5E/6
10M mode 140m, CAT5E

## Slide 30
Plug & Play
Plug
Play

## Slide 31
Quick Add 3rd Party IPC
Uniview NVR use private protocol to add Hikvision and Dahua IP camera, and user don’t have to check and fill in the port number, user name and password, they will be filled automatically, only thing you have to do is to click “Add”

## Slide 32
Live Video When Managing IP Camera
When the you are managing the IP Cameras on NVR HMI, you can call the live video in the setting menu to see what is in this channel, so you can make it much easier if you want to change the channel name

## Slide 33
High Speed Of IPC Connection
 | Uniview | H Company
Batch search(34 pcs of IP Camera) | 1.6s | 4.2s
Batch delete(32 pcs of IP Camera) | 7.04s | 11.74s
IPC offline, reconnect speed | 18.08s | 38.55s
NVR reboot, preview resume speed | 72.14s | 125.82s
Uniview NVR has high speed of IP Camera search, delete, reconnection.
Here below is the average time of five times testing.

## Slide 34
Configure Image Parameter of IPC on NVR
With UNV NVR, you can easily do configuration of the image parameter of IPC on NVR directly, no need to open the web interface of IPC
Image Parameter | Uniview | Hikvision | Dahua
Brightness | √ | √ | √
Saturation | √ | √ | √
Contrast | √ | √ | √
Hue | √ | √ | √
BLC | √ | × | ×
Focus | √ | × | ×
Day and Night | √ | × | ×
Exposure | √ | × | ×
Sharpness | √ | × | ×
WDR | √ | × | ×
White Balance | √ | × | ×
Defog | √ | × | ×
DNR | √ | × | ×
The image parameter which Uniview and other manufacturers support to configure on NVR

## Slide 35
Easy to Access Web Interface of IPC
Sometimes you may have to access the web page of IP camera to do some configuration which NVR can not control on human interface.
If the IP camera was connected with the NVR via switch it is easy to access.
But what if it was connected to PoE ports of NVR?
1.Unplug the IP camera from the PoE ports
2.Connect IP Camera to switch and power on again
3.Change the IP address as the same segment as your PC and access the web interface of the IP Camera
1.Open the web interface of NVR, click “Access”
2.Directly access into the web interface of IP Camera
Access
Other Manufacturers
UNV
No Unplug and Plug, Easy to use

## Slide 36
Build-in DC12V Output
NVR208 series
NVR308 series
DC12V
Build-in DC12V output ports in the NVR208 and NVR308, some alarm in or alarm out device can directly get power from the NVR, make the installation of the external device much easier

## Slide 37
Easy to Use

## Slide 38
Drag Preview Window Directly
You can easily drag the preview window in preview interface directly, it makes it much easier if you want to interchange the channels

## Slide 39
Corridor Mode
3
5
7
Easy to support IP Cameras that working under corridor mode
User can also play back in corridor mode
Double the useful monitoring area

## Slide 40
USB 3.0
Uniview NVR featured with USB 3.0, compare to traditional USB 2.0 in other company, USB 3.0 has about 10 times higher data download speed than USB 2.0
30GB video recording files
1 Hour
5 Minutes
USB 3.0
USB 2.0

## Slide 41
SATA 2.5
SATA 3.0
Up to 300Mb/s
Up to 6Gb/s
High possibility of Frame loss、Video loss、Video freezing
Fluent Preview and Playback, high reliability on video recording
SATA 3.0

## Slide 42
Instant Playback
What if the user see something happened in preview window, and you want to instantly do playback to check it?
UNV NVR support Instant Playback function to solve this problem perfectly
Event been watched on preview window
Wait until recording packed and finished
Go to playback interface and do playback then
Normal Playback
Instant Playback
Instantly playback in preview window
UNV NVR support up to 5 minutes instant playback

## Slide 43
Smart Search
You had to take hours to search the whole playback bar to find the desired video clip
What if you want to find out the area where a motion objects or person has passed?
Specify an interesting area and do smart search, Just take seconds to find the desired video clip
Normal Search
Smart Search

## Slide 44
Double Playback Progress Bar
Channel 1
Channel 2
Channel 3
All Channel in Sync Playback
More visual for users

## Slide 45
Instant Preview on Playback
User can easily preview the thumbnail picture of the corresponding time when the cursor put on the playback bar

## Slide 46
Easy Internet Access
Scan QR Code on NVR
Play on Smart phone
Indicator lamp turned on when get into internet

## Slide 47
Internet Explorer Compatibility

## Slide 48
Easy Maintenance

## Slide 49
Reset IPC on NVR
If there are any IP camera which need to be reset to factory settings, you don’t have to get into web interface of the IPC or climb up to push the reset button, with Uniview NVR, you can just reset the IPC directly on NVR

## Slide 50
IPC Information
You can get the IPC information including the Vendor information, Model name, Firmware version, Serial Number and other information from the NVR, the user don’t need to get into the IPC web interface to check those information.

## Slide 51
Upgrading IP cameras from NVR directly, make the system maintenance easier & more convenient
IPC Upgrade on NVR
Upgrading IP cameras from NVR with the firmware in USB disk
Upgrading IP cameras by just clicking “cloud upgrade” on NVR, available on human interface and web interface (NVR should be able to access internet)

## Slide 52
Cloud upgrade
Ask technician of the manufacturer for the latest firmware
Technician upload the firmware to ftp (Maybe make mistake here)
Download the firmware (Maybe make mistake here)
Plug-in the USB Disk or open the webpage (Maybe failed here)
Finish the upgrade process
Annoying process and easy to make mistake
Easy, Fast, Unmistakable
Just click “upgrade” in the NVR menu
Cloud Upgrade
Other Manufacturer
Uniview
Auto detection of the latest firmware and upgrade successfully

## Slide 53
Typical Application

## Slide 54
Typical Application

## Slide 55
Thank you!